## Slide 1: Feed Bins & Dosing
Technical Development Program for PPE, 2014-2015

## Slide 2
2
Provide stable mass flow for the raw mill
  Optimal energy utilisation
  Maximum availability & reliability
Achieve the right mix
  Chemical targets
  Homogeneity
Buffer storage after reclaiming
Process Integration

## Slide 3
3
Feed bin problems are a major cause for mill problems (damages, low production rate, gearbox failures)!
  Segregation
  Erratic flow
  Blockages
  A process chain is only as strong as its weakest link
Importance of Feed Bins & Dosing

## Slide 4
4
Feed Bins
Feed Bins & Dosing

## Slide 5
5
Various problems are a result of bad feed bin design
  Incomplete emptying and reduced bin live capacity
  Inconsistent material reclaim rate
  Varying product quality and loss of production
  Need for dangerous manual cleaning action
Wrong Feed Bin Design

## Slide 6
6
Always design feed bins for mass flow
To achieve this, a feed bin has to be designed according to the material properties, which depend on:
  Particle size distribution
  Moisture content
  Chemical composition
  Particle shape
  Temperature
  and other parameters…
Correct Feed Bin Design
Funnel flow
Mass flow
X

## Slide 7
7
The main properties for feed bin design are:
  Abrasiveness
  Flowability
    Determined by shear tests
    Flowability generally decreases with increasing fines and moisture
Correct Feed Bin Design

## Slide 8
8
Internal friction
  Describes tendency to bridge and thus define the required minimum bin outlet dimensions
  External friction
  Describes tendency to stick and thus define the required minimum wall inclinations and suitable internal wall lining material
Correct Bin Design – Shear Test
N/Nx: Normal compressive
load
T/Tx: Shear torque
1 : Base ring
2 : Upper ring
3 : Cover
4 : Sample of bulk solid
5: Sample of wall material
Shear plane

## Slide 9
9
Valley angle
  The common inclination formed by two inclined planes is the lowest inclination!
Rounded corners reduce the risk of sticking material
Wall Inclination

## Slide 10
10
Segregation cannot be avoided when feeding a bin
  It is normally compensated in mass flow bins
Eccentric feeding points can cause excessive segregation and thus affect product uniformity
  Relocate feed point to the centre
Segregation

## Slide 11
11
Expanding design for full outlet activation
Bin outlet activation if required
  Oscillating feeder
  Discharge arm
  Rotating screw
Discharge aids only as corrective measure and carefully used. Danger of further compaction!
  Aeration
  Vibration
Feed Bin Outlets

## Slide 12
12
Dosing
Feed Bins & Dosing

## Slide 13
13
Dosing = Feeding + Measuring + Control
Use gravimetric feed systems
Repeatability
Accuracy
Know the relevant time basis to assess dosing performance
  For raw mill feed: approx. 10min (depending on mill)
Theory of Dosing
Feeding
Measuring
Control

## Slide 14
14
Impact flow meter (not recommended)
Coriolis flow meter (Schenck Process®)
Rotor scale with integrated feeder (Pfister®)
Flow Measurement for Fine Materials

## Slide 15
15
Constant belt tension
  Proper belt alignment
  Clean and functioning tensioning station
Constant belt stiffness
  No metal splice
  No skirted belt
  No belt damages / patches
Reliable and clean belt speed sensor
  On a 100mm diameter wheel, coating of 0.5mm results in
  a weighing error of 1% !
No material build-ups, spillage or equipment on weighing mechanism
Belt Weigh Feeder - Maintenance

## Slide 16
16
Targets for belt weigh feeders
  Turndown ratio min. 10:1
  Long term accuracy better than +/- 0.5%
  Short term accuracy better than +/- 1.0%
  Response to set point changes < 10 % shall be less than 1 min.
Achieve these targets through
  Maintaining your equipment in a clean condition
  Calibration (and documentation)
    On regular basis
    After changes on equipment or material
    When readings are suspicious
Targets

## Slide 17
17
Coriolis flow meter  with tube calibrator
Rotor weigh feeder  with pre-bin
Online Calibration (loss-in-weight)

## Slide 18
18
Belt weigh feeder calibration by:
  Test weight method
  Volumetric measurement
  Loss-in-weight method
  Drop test (load on truck)
Offline Calibration
Details on calibration methods