## Slide 1: Process Fans
Technical Development Program for Process Performance Engineers – SPREAD 2106
Mirko Weber

## Slide 2: FAN Initiative “FANi” in exHolcim - Background
Large process fans are responsible for about 30-50% of the electrical energy consumption in cement plants.
Experiences in the past and actual measurements have shown that fans often run below the expected fan efficiency of 75-85%.
Besides fan efficiency, the power consumption is proportional to the flow in a fan system, therefore any source of undesired flow (i.e. false air intakes) shall be fixed.
Expected benefit if 1% efficiency increase per main fan: 30 million USD by fan performance optimization
Further economical benefits by:
  Increased production capacity in sold-out markets
  Increased AFR utilization potential group wide

## Slide 3
3
Agenda
Fan Basics
3
Fan Efficiency
19
Fan Assessment
28
Fan Issues and Maintenance
45

## Slide 4
4
Fan Basics
Fan and Plant Characteristic
VSD vs. Fixed Speed
Flow Phenomena
Technical Development Program for Process Performance Engineers 2015

## Slide 5: Fan and Plant Characteristic
The fan operates at the crossing point of plant and fan characteristic
plant characteristic
design point
fan characteristic
VD
pD
Dp
Vact
P
fan characteristic
PD

## Slide 6: Gas Density Impact (1/2)
p
D
V
The fan curve is a result of the fan geometry, at a given gas density and fan speed
Design point
Fan characteristic
VD
rreference ≠ ractual
ractual < rreference  fan capacity reduction
Same fan speed
DpD
DpD,real

## Slide 7: Gas Density Impact (2/2)
The power curve depends also on the gas density
Design point
VD
PD
fan characteristic
P
PD,real
V

## Slide 8: Control Methods: Variable Speed Fan (VSD)
p
D
V
design point
plant characteristic
100% fan speed
fan characteristic
operating point
pO
To reach the set point (operating point) the fan speed can be modified  shifting the fan characteristic
reduced fan speed
VO

## Slide 9
9
Fan Characteristic: Fan Speed Impact (VSD)
volume flow
static pressure
power requirement
first approach, as equations do not consider changes in density, compressibility and efficiency

## Slide 10: Control Methods: Fixed Speed Fan
VO
p
D
V
design point
additional Dp by throttle
plant characteristic
100% fan speed
fan characteristic
To reach the set point (operating point) the gas flow has to be throttled by a damper  tilting the plant characteristic
operating point
pO

## Slide 11
11
Remember for VSD:
vO
design point
plant characteristic
100% fan speed
fan characteristic
operating point
reduced fan speed
pO
power required with VSD
Dp
v
Power Consumption: VSD vs. Fixed Speed
V

## Slide 12
12
vO
additional Dp by throttle
design point
plant characteristic
100% fan speed
fan characteristic
operating point
pO
Additional Dp leads to increased power consumption
power required with fixed speed fan
power required with VSD
VSD fans are much more efficient than fixed speed fans
Dp
v
Power Consumption: VSD vs. Fixed Speed
V

## Slide 13
13
Almost no fan can provide the desired continuous, steady flow over the full range of volume flow, pressure and rotating speed
If your fan shows the following symptoms
  oscillation/variation of flow and pressure
  increased noise and/or vibration levels
  increased gas temperature difference between fan inlet and outlet
  reduced efficiency
Most likely one of the known flow phenomena occurs
  surge
  stall
  …
Fan Flow Phenomena

## Slide 14
14
The fan should always be operated right of the fan curve peak pressure
  Increasing flow  pressure capacity decreases
  Safety margin: operate at minimum 110% “peak pressure”-flow
Surge
Dp
v
range of operation
surge limit
If the fan is operated left of the fan curve peak pressure:
  with increasing flow also the pressure capacity increases
  the energy imparted to the gas alternates between a) creating kinetic energy (increased flow and velocities) b) potential energy (compressing the gas)
  the operating point is not defined

## Slide 15
15
Surge

## Slide 16
16
Effects of surging
  variation in fan delivery pressure
  variation in volume flow => the fan is pumping
  even flow oscillation => the fan volume flow gets “negative”; the flow is exiting the fan inlet
  high heat generation => the fan efficiency significantly decreases
  increased noise generation => might sound like “whoosh” or “whoomp”
  increased vibrations => structural fatigue damage to the fan => damage to ductwork and other system components
The fan is not suitable for this operating point
Surge

## Slide 17
17
The higher the fan outlet pressure, the more dense is the gas
Gas fluid particles experience this like a “traffic jam”
  particles are forced to stop => the fan volume flow suddenly decreases
  then again there is room to move => the fan volume flow suddenly increases again
  some particles are forced to make a detour, leaving their ideal trajectory => this needs extra energy and makes the traffic jam even worse
  some particles are forced to break away, stop, go back and queue again => this recirculation drastically reduces the fan volume flow, eventually more particles are going back than forth
  particle crashes and friction between particles are unavoidable => heat generation, vibration and a increased noise level are the consequences
Stall

## Slide 18
18
Stall

## Slide 19
19
Effects of stalling
  variation in fan delivery pressure => the pressure falls off
  variation in volume flow => the fan is pumping
  even flow oscillation => the fan volume flow gets “negative”; the flow is exiting the fan inlet
  high heat generation => the fan efficiency significantly decreases
  dramatic noise generation => might sound like solids are hammering the blades => the fan efficiency significantly decreases
  significant vibrations => structural fatigue damage to the fan => damage to ductwork and other system components
Stall

## Slide 20: Common Effects of Surge and Stall
There are common effects and influences
  variation in fan delivery pressure  the pressure falls off
  variation in volume flow  the fan is pumping
  flow oscillation  fan volume flow might become “negative”, is exiting the fan inlet
  high heat generation  the fan efficiency significantly decreases
  dramatic noise generation  sounds like “whoosh” (Surge) or like solids are hammering the blades (Stall)
  significant vibrations  structural fatigue damage to the fan  damage to ductwork and other system components
Counteraction: increase flow / change operating point!

## Slide 21
21
Fan Efficiency
Definitions
Impact of Dust
Impeller Types
Technical Development Program for Process Performance Engineers 2015

## Slide 22
22
Power Consumption of Fan System
BLACK BOX

## Slide 23
23
Power Consumption of Fan System

## Slide 24: Calculation of Shaft Power Requirement
V
Dp
Dp
V
P
Pshaft ≠ PMeasured
P
Typical values:
hTransformer = 99.0%
hVSD = 97.5%
hCable = 99.5%
hMotor = 96.5%
hCoupling = 100%

## Slide 25
25
Shaft power (as calculated process-wise)
Total power (as measured electrically)
Power consumption – some definitions

## Slide 26
26
Fan Efficiency
in case of significant dust load additional shaft power to be considered
for detailed calculation application of fan tool recommended

## Slide 27
27
Fan Efficiency with Dust Impact

## Slide 28: Fan Efficiency Field
100% fan speed
design point
VD
pD
fan characteristic
The fan efficiency h is typically at the optimum near design point
VO
operating point
pO
reduced fan speed
With VFD the efficiency field moves with shifting the fan characteristic, such the fan efficiency is high in a wide operating range

## Slide 29
29
Impeller Types, Efficiency and Dust Load

## Slide 30
30
Efficiency vs. Build-Up Risk
steep blades (large b1, b2)
lower efficiency
lower build-up risk
b2
b1
b2
b1
flat blades (small b1, b2)
higher efficiency
higher build-up risk

## Slide 31
https://sites.google.com/a/holcim.com/cp-internal-training-work-site/
Fan Efficiency Tool (FET) and Fan Benefit Calculator (FBC)

## Slide 32
32
The Fan Assessment Process
Tools
Selection of Measuring Points
Required Process Data
Fan Inspection
Fan Assessment
Technical Development Program for Process Performance Engineers 2015

## Slide 33
33
Complete study of process fan performance
  Fan Performance
  Mechanical Condition
Proposals for improvement (if necessary)
  Process
  Maintenance
  CAPEX
Results verification
What is a Fan Assessment

## Slide 34
34
Suspicion of sub-normal operation
  Higher power consumption
  High vibrations
  Reduced gas handling capacity
Need to know equipment limits
  Bottleneck analysis
  Upgrade projects
When to perform a Fan Assessment

## Slide 35
35
Fan Assessment Process:
Pre work

## Slide 36
36
Before field work:
  H&S !
  Documentation gathering
    Fan curves + Reference conditions
    Fan drawings (Impeller, inlet cone, casing)
    Arrangement drawings / pictures (Inlet & outlet ducting, installation…)
    …
  Selection of the best flow measurement location and instruments
  Measuring ports checking and installation
Fan Assessment Process: Steps (1/3)
Remember: Wrong documentation will lead to wrong conclusions!

## Slide 37
37
Field work:
  Process Measurements:
    Volume flow at fan inlet or outlet (both if possible, consider false air!)
    p at fan inlet and outlet
    T at fan inlet and outlet
    Power consumption & fan speed
  Visual inspection:
    Blades condition (thickness, length, deformation, wear…)
    Inlet cone penetration
    Cone – Impeller Gap
    Build-ups (take pictures, take samples, hard/soft?)
    Check for over-heating or corrosion signs (also on the casing)
Fan Assessment Process: Steps (2/3)
Guide value to be provided by fan supplier
Remember: Wrong measurements will lead to wrong conclusions!

## Slide 38
38
Hardware
  Camera
  Manometer (with data logger)
  Thermometer (with data logger)
  Gauge / Measuring tape
  Flow measurement devices
    Prandtl / Pitot
    Promecon
    Anemometer
Software
  Fan Efficiency Tool (FET)
  TIS-FET
  Anemometer and Prandtl Tube Measurements Spreadsheet
Tools

## Slide 39
39
Field Work: Selection of measuring points
3*D
Pressure gauge
Temperature gauge
Ideal:
  Straight distance 5*D before and 3*D after
  no obstruction, joint or change in gas path
  At least two openings at 90° (better four for large ducts)
  Safe and easy access

## Slide 40
40
Pressure Measurement
Measuring ports
To Pressure Sensor
Round duct
Squared duct
Pipe

## Slide 41
41
Measured Values:
  Fan Speed (taken from CCR)
  P (at VSD, taken from CCR)
  Vinlet (e.g. Prandtl tube)
  Pinlet/Poutlet
  Tinlet/Toutlet
Recommendation
Crosscheck measured flow!
  Measure at inlet and outlet
  Consider false air from measuring point(s) to fan inlet/outlet
Field Work: Process data - Example

## Slide 42
42
Inspection
  Casing – specification and conditions
  Inlet cone - impeller gap and cone penetration
  Impeller conditions (wear, deformation…)
Document your findings!
Fan Inspection

## Slide 43
43
Cone / Impeller gap
  Specific value given by supplier
  General reference: 7.5 mm (for impellers bigger than 2m)
Cone penetration
  Specific value given by supplier
  General reference: 25 – 50 mm
Inlet Cone Inspection

## Slide 44
44
Correct fan inlet cone radial (gap) and axial placement (penetration) is crucial for high fan performance / efficiency by creating
  a laminar flow at fan inlet
  a recirculation
During maintenance adjust fan gap
  according supplier specification
  considering thermal expansion
Fan Gap Management
Source: Howden

## Slide 45
45
Desk work:
  Measurement data compilation
  Fan efficiency calculation
  Data comparison (check next slides)
    Expected = Calculated?
    PExpected = PMeasured?
    VEexpected = VMeasured?
  Conclusions
    Match visual inspection with measured / calculated data
  Corrective actions
    Get aligned with maintenance department
Fan Assessment Process: Steps (3/3)
Remember: Performance will only improve if you work as a team with maintenance!

## Slide 46
46
Accuracy Category 1: Holcim standard
Accuracy Category 2: in case of insufficient indications
Fan Accuracy Classes

## Slide 47
47
design point expected performance
plant characteristic
fan characteristic
100% fan speed
vD
pD
Dp
v
fan accuracy
measured point
to be accepted
measurement accuracy
- Measurement uncertainty
- Accuracy class tolerance
Acceptable
Not Acceptable
Consider impact of chosen accuracy class for Fan Guarantee & Performance Test
Fan Accuracy Classes

## Slide 48
48
YES
NO
GOOD!
Check
Motor h
Damper Position
Build-ups?
Check
Impeller
Fan Assessment

## Slide 49: Fan Inspection
Check the Fan Inspection Video
  https://drive.google.com/a/holcim.com/file/d/0B6fe5NZGsbbYYXFRcG01QnNTbEU/view?usp=sharing

## Slide 50
50
Fan Issues and Maintenance
Technical Development Program for Process Performance Engineers 2015
Workshop Inspection
Peak Temperature and Interlock
Fan Brakes
Wear and Wear Protection
Build-up, Vibrations and Cleaning
Modification and Replacement

## Slide 51
51
Quality assessment of a main process fan has to be carried out at Workshop before assembling of impeller and shaft
  visual inspection
  magnetic particle test of impeller and shaft
  ultrasonic inspection of shaft
  hardness test on shaft
  materials check
  dimensions check
  verification of welding and heat treatment (if applicable)
  review of documents and certificates
  balancing test
Workshop Inspection of New Fan
Caution! Workshop inspection is crucial to ensure that we get what we pay

## Slide 52
52
Common sense (and physics) says: a) Tgas, expected ≤ Tfan, 100% time < Tfan, short time <T fan, peak = max b) gas temperature UP  fan lifetime DOWN
Never accept a fan without written (signed) datasheet including:
  Peak temperature, which never shall be exceeded
  Temperatures the fan can be operated for short periods (up to 10 minutes)
Implement / adjust fan interlock to protect fans and people
  Never override a safety interlock!
Consider and check measures to prevent fan overheating
  Emergency fresh air
  Water injection
Fan Peak Temperature & Interlock

## Slide 53
53
How to slow down/stop the fan faster to get sooner access for inspection and maintenance? How to prevent the fan from turning while doing inspection and maintenance (H&S)?
Fan Brake
Electrical Brake
  only possible with “4 quadrant drive VFD“-type
  however, due to power-off / lock-out during maintenance even this VFD cannot be used for preventing fan rotation
Mechanical Brake
  wait until fan stopped, then prevent rotation by blocking the impeller with wooden beams
  do not brake the fan by pressing a wooden beam against the fan shaft (H&S)
  better: install mechanical fan brake

## Slide 54
54
Erosion / Wear Root Causes
  corrosion
  abrasive dust
  high fan speed and high fan inlet velocity
  blade-hitting gas/particle flow due to duct/fan design
  inappropriate blade shape and angles
  soft blade surfaces
Erosion and Wear
High fan speed is the most important driver for Wear on Blades
  wear varies in the second up to third power of the speed of a particle that hits the blade

## Slide 55
55
Direct Protection
  increased thickness of wear parts
  direct hard surfacing
Protection by Wear Plates
  mild steel corners and plates
  abrasion resistant steel plates
  mild steel plates with hard surfacing
Particle Deflection
  deflector plates
Wear Protection

## Slide 56: Wear Protection by Particle Deflection
without
with
Deflector

## Slide 57
57
Example of Wear and Deflector Plates
wear plate
deflector plates

## Slide 58
58
Build-Up Root Causes
  high gas temperatures (> 350 … 400 °C)
  mineralogical composition of raw mix (clay, iron)
  high fan speed and high fan inlet velocity
  blade-hitting gas/particle flow due to duct/fan design
  inappropriate blade shape and angles
  dew point problems
Build-up and Vibrations
Unstable/unbalanced Build-Up leads to Fan Vibrations
  increased stress on equipment
  reduced lifetime of equipment
  increased maintenance required
  short interval of kiln stops for fan cleaning
  loss of production
  increased thermal & electrical power consumption
days

## Slide 59
59
Example of Build-Up

## Slide 60
60
High pressure water spray
Steam injection
Compressed air injection
Sand blasting
Acoustic resonance (ultrasonic)
On-Line Fan Cleaning (during operation)
NOTE: Success of the above methods is difficult to predict! No general recommendation.

## Slide 61
61
Cracking the dust layer
compressed air water steam
compressed air water steam

## Slide 62
62
Sand Cleaning Device
Reduce speed during cleaning

## Slide 63
63
Acoustic Cleaning Devices
acoustic horn
acoustic horn

## Slide 64
64
On-Line Active Balancing System
  balancing ring (actuator) which is mounted on fan shaft
  stator with coils which is mounted concentrically around balancing ring at the bearing housing
  actuator contains two identical balancing rotors actuated by coils in the stationary part using stepping motor principle
  balancing rotors fixed by magnetic forces
  sufficient air gap between the two parts allows for free shaft movement
Source: Hofmann Mess- und Auswuchttechnik GmbH & Co. KG (former: LORD Active Balancing System)

## Slide 65
https://sites.google.com/a/holcim.com/cp-htec-cm-fani/09-technical-solutions/active-balancing-system
http://www.youtube.com/watch?v=qot5Ydp8Z10
On-Line Active Balancing System

## Slide 66
66
Very positive feedback of competitors’ plants, who suffered from vibrations on kiln ID fans and installed active balancing:
  time between fan/kiln stops for cleaning increased from less than 2 months up to one year
  vibrations constantly kept below 2 to 5 mm/s
  maintenance requirements for the system almost zero
  payback period some few months only
In 2009 the active balancing was implemented for the first time in Holcim - at Ambujanagar plant at 3 kiln ID fans:
  time between cleaning stops has been more than doubled
  payback was some 6 months
  zero maintenance
  balancer works very reliable and fast
Other references were following within the Group (Höver, Naragong, ...)
On-line active balancing is currently the most promising solution to minimize impact of fan build-up
On-Line Active Balancing System

## Slide 67: Successful Implementation in Narogong
Fan cleaned ~ every 2 month
No kiln stop related to fan vibration after installation!
Installation of autobalancer

## Slide 68
68
“Simple” solution to increase impeller diameter and as such pressure capacity
Feasibility depends on blade type, impeller geometry, space restrictions, critical fan speed, …  contact your fan supplier
Cheaper than new impeller with correspondingly larger diameter, but in comparison usually with some drawbacks:
  lower pressure/flow capacity
  lower efficiency
  more susceptible to vibrations
Fan Impeller Tipping
Caution! Improper tipping may lead to structural damages and personnel injuries

## Slide 69
69
Why?
  Poor mechanical condition and/or poor efficiency of existing impeller
  Increased flow/pressure capacity required (rate increase, AFR – before concluding: check false air)
  Significant change of normal operating point (by WHR, lower PRI…)
Cheaper than complete new fan system, however, potential for higher capacity limited and reduced fan efficiency to be accepted:
  Flow capacity ~ + 10%
  Pressure capacity ~ + 20%
  Efficiency ~ - 3%-points (compared to new system)
Still major modifications required:
  housing
  inlets
  shaft seals
  coupling
  bearing units including temperature sensors
  …
Fan Impeller Replacement

## Slide 70
70
Assessments are needed to know actual fan performance
Reference conditions are crucial to get right conclusions
Wrong documentation will lead to wrong conclusions
Wrong measurements will lead to wrong conclusions
Visual inspection is crucial to find the root causes
Be sure that you have all the data before concluding
Performance will only improve if you work as a team
Summary

## Slide 71
71
Questions????
Holcim FANi page: https://sites.google.com/a/holcim.com/cp-htec-cm-fani/home

## Slide 73
73
  Consider p, V and P reserves on expected operating points
    e.g. kiln ID fan (new line): 30% flow, 30% pressure, 10% power
    choose appropriate fan accuracy class
  Consider the right gas temperature and density
    consider peak operating temperatures: lifetime, interlock
    design gas density: dust, T, O2, CO2, H2O
  Choose the appropriate fan blade design
    consider dust, build-up risk, efficiency
    use aerofoil blades only for clean gas applications
  Use VSD with direct connection of motor and fan
  Prefer larger impeller diameter, lower max fan speed
    < 1‘000 rpm for large fans; < 3‘600 rpm for e.g. clinker cooler cooling air fans
  1st critical fan speed minimum 150% of max fan speed
  Check fan curve (surge, motor and speed limits)
  Do workshop inspection
The right Fan Design is crucial for fan performance

## Slide 74: Location of pressure measurement planes for site testing
Source of drawing: ISO 5802
We specify conditions at (4) and (8) dynamic differences are ignored because of same/similar gas velocities in ducts
2a
Supplier typically specifies conditions at (1)/(1a) and (2)/(2a) and sometimes ignores losses from (4) to (1a) and from (2a) to (8)
1a
(1a = impeller inlet)
(2a = fan outlet)

## Slide 75: Measured vs Expected – Example (Fan Efficiency Tool results)
hVSD = 97.5 %
hCable = 99.5 %
hMotor = 96.5 %
hCoupling = 100 %
PM,S = 182 kW (at Shaft)
DpM = 19.6 mbar
VE = 256’029 m3/h = 71.1 m3/s
PE = 169 kW
From Process Measurements
From Fan Curves
DpM
PE
VE
VE
VM = 185’427 m3/h = 51.5 m3/s
PM = 190 kW
DpM = 19.6 mbar
(at Shaft)
(at VSD)

## Slide 76: Graphical Representation of Results - Example
Error Bars from Accuracy Class
Error Bars from Measurement Accuracy
Error “Areas” overlapping?
Yes  Acceptable
No  Not Acceptable

## Slide 77: Conclusions
Possible causes
  False air not considered?
    Measurement location
  Damaged impeller, casing or cone?
    Worn out blades
    Cones not properly adjusted
Findings
  Moderate to high flow deviation (-18 to 0%)
  High efficiency deviation (-26 to -13%)
  High power deviation (18%)
Notes: First, we have to gather the findings:
The fan is delivering much lower flow than expected
The efficiency is poor
And the fan is consuming more power than expected but it’s still inside the tolerance.
What could be the root causes?
The first one is that we didn’t consider FA for the assessment, there might be a big source of false air from the measuring point to the fan outlet
The fan is working at 60% of the max fan speed, this can create an error because of the calculation method, which we cannot really avoid but we should be aware of and it can create also a high efficiency drop, not following the rule of the “constant” efficiency for VSD anymore.
The third preliminary conclusion we can get (without checking the fan itself) is that there might be some damages on the impeller, like wear or a problem with the gap adjustment.

## Slide 78: Recommendations
Check impeller
  Inlet cone / impeller gap
  Inlet cone penetration
  Impeller conditions (wear, deformation…)
Crosscheck measured flow
  Measure at inlet and outlet
  Consider false air from measuring point(s) to fan inlet/outlet
Notes: And these would be the recommendations we can make out of the conclusions from the tool results.
Check the impeller and cross check the measured data
In this case, we found out that the impeller conditions were quite good, but there was a significant amount of false air coming in. When we remade the calculation considering this “extra” flow, we found out that the efficiency of the fan is actually good and that the problem is not on the impeller but on the ducting.
Final message, before suggesting to change the fan, make sure you don’t have another problem that is much cheaper and easier to fix.