## Slide 1: NOx Emissions Control & Reduction
Technical Development Program for Process Performance Engineers – SPREAD 2016
Mirko Weber

## Slide 2
2
Why do we care about NOx?
  Environmental impacts
  Holcim emissions targets
  Legal limits
Where is the NOx formed?
  Thermal and Fuel NOx
  Influencing factors
How NOx can be reduced?
  Primary measures
  Secondary measures
  New developments
Content

## Slide 3
3
NOx contributes to acid rain
  damage to vegetation, aquatic life
NOx is affecting ozone (O3) balance
  precursor for photochemical smog contributors (ozone, “PAN”, HNO3 etc.) in troposphere  damage of the human respiratory system (lungs)
NOx can contribute to eutrophication
  Influence of ecosystem by nutrient overload
NOx is a risk for human and environment

## Slide 4
4
Environmental regulation - A continuous evolution…
1800 – 2200 mg/Nm3 before 10.2007
1200 mg/Nm3 10. 2007 – 01.2008
800 mg/Nm3 01.2008 – 03.2012
600 mg/Nm3 since 03.2012
500 mg/Nm3 starting 2016
Source: Marco Bestetti
200 mg/Nm3 ? (Germany, Incinerators)
Example Holcim Italy

## Slide 5
5
NOx emissions plausibility check NOx in mg NO2/Nm3, dry @ 10% O2
Standard deviation of hourly averages is 20 - 50%
NOx emissions of 350 to 1200 mg/Nm3 @ 10% O2 expected
> 2000 | extreme emissions, measurement to be verified
1200 to 2000 | high emissions but possible
350 to 1200 | normal emissions range
< 350 | unlikely without any special conditions

## Slide 6
6
NOx units can be misleading…
ppm NO1
400
What is measured by the analyzer
* 2.1 Nm3/kgcli at 3300 MJ/tcli and 10% O2
* 0.7 kgcli/kgcem. material
g/tcem.materials NOx
1020
Transformation into ERT Units
820 8% actual O2
* 2.05 mg NOx (as NO2)/ ppm
What you read from the analyzer (depending on analyzer type)
mg/Nm3 NOx at actual O2
mg/Nm3 NOx at 10% O2
695
Transformation into Standard Units
* 11 / (21 – actual %O2)
1 ~95% of the cement kiln NOx emissions are in form of NO, the rest as NO2. Nevertheless NOx is commonly expressed as NO2!

## Slide 7
7
NOx Emissions expressed in mg/Nm3 dry
Conversion:
Conversion ppm NO to mg NO2 - Step by step calculation
* Dry or wet according to measurement principle (in situ, extractive) ** water content of gas (vol %)
NOx Emissions expressed in mg/Nm3 NO2*
NOx Emissions expressed in mg/Nm3 dry @ y % O2
NO measurement (in ppm)
?
Conversion: ppm x 2.05 = mg/Nm3
O2 correction:
NOx Emissions expressed in mg/Nm3 NO*
Conversion: ppm x 1.34 = mg/Nm3
Conversion: mg NO x 1.53 = mg NO2

## Slide 8
8
Main flame at T>1500°C from N2 in the air
Thermal NOx
In the calciner / secondary firing from fuel nitrogen
Fuel NOx
Fuel-N
Intermediate products HNCO etc.
HCN
NOx
NHx radicals
Air-N2
N N
There are two main NOx formation mechanisms (simplified)

## Slide 9
9
Temperature, Oxygen, Air and Fuel Nitrogen to form NOx
Fuel bound nitrogen  Fuel NOx
(T ~900°C)
N2, O2 in air  Thermal NOx
(T >1500°C)
*Fuel NOx formation in the main firing is hampered because the O2 is preferably used for combustion and not available for oxidization of the fuel nitrogen.
*
Small NOx quantities from raw material

## Slide 10
10
Becomes more important the more stringent the limit
Not treated by reduction technology (beside SCR)
Raw Mix expulsion test example  75±30 [mg NO2 / Nm3]
NOx from raw material proportionally low, but not treated

## Slide 11
11
Main factors favoring NOx formation at main burner (1/2)
  Availability of oxygen
    High overall excess air rate (Kiln inlet oxygen)
    High degree of turbulence (high axial and tangential momentum, retracted burner position)
    Weak Internal Recirculation Zone (IRZ)
    High fuel transport air (in the center of flame)
    Delayed ignition and burn out of fuel (low reactivity of fuel, i.e. low percentage of volatiles, low fineness or big droplet size)
The more Oxygen the higher is the NOx formation
+
+
_
Secondary air
Secondary air
Axial
Axial
Radial/Swirl
Radial/Swirl
Central

## Slide 12
12
Main factors favoring NOx formation at main burner (2/2)
  High flame temperature
    High burning zone temperature (hard burning regime)
    High calorific heat value
    High axial / tangential momentum (strong flame)
    High and frequent temperature peaks (process instabilities)
    High secondary air temperatures
    High residence time at high temperature (long, but strong (hot) flame / low fuel volatiles)
The higher the Main Flame Temperature the more NOx
N2 + O2  2 NO d[NO]/dt = 2 K1 [N2] [O]

## Slide 13
13
Main factors favoring NOx formation in calciners
  High oxygen availability (excess air rate / tertiary air, fuel arrangement)
  High nitrogen content of fuel
Oxygen and Fuel Nitrogen raise NOx formation in calciner

## Slide 14
14
Main influences on NOx formation
Fuel mix characteristics and pyroprocess operation determine NOx emissions
 | Thermal NOx | Fuel NOx
Temperature | +++ (T > 1500 °C) | +*
Overall Excess Air Rate (O2) | ++ | ++*
Residence Time | + | +
Nitrogen content in fuel | + | ++
Volatile matter in fuel | +* | +*
* High influence on NOx reduction mechanism

## Slide 15
15
Reduce NOx “precursors”
Reduce NOx production by modification of existing process
Convert NOx to N2 by adding an additional gas cleaning unit
Three steps to reduce NOx – Start on top!
Secondary Reduction Measures
Primary Reduction Measures

## Slide 16
16
Improve process stability (process optimization, expert system)
Adjust excess air (kiln inlet and calciner oxygen)
Optimize burner operation (transport air, primary air)
Improve kiln feed burnability (feed mix, fineness)
Avoid overburning (strict control of clinker free lime, target >0.8 %CaO)
Reduce NOx formation in main burner by avoiding high temperatures and excess oxygen

## Slide 17
17
  Transport air diminished from 1900 to 1180 Nm3/h Coke load increased from 3.2 to 5.1 kg/Nm3
  Primary air (excl. transport air) reduced from 18% to ca. 12%
  New burner tip
  NOx reduced from ca. 1500 to 1200 mg/Nm3, dry @ 10% O2 (100% petcoke)
  NOx reduced form ca. 900 to 700 mg/Nm3, dry @ 10% O2 (bit-oil / petcoke mix)
Merone: Burner modification achieves ~20% NOx reduction
D2
D1
D2
Radial air
Petcoke
Axial air

## Slide 18
18
NOx = 100%
NOx = 97%
NOx = 90%
Burner settings: Transport air quantity optimization
Burner settings: Primary air quantity optimization
Eclépens: Burner settings optimization reduces NOx (~10%)
NOx = 97%
Bottleneck
NOx = 124%
NOx = 100%
NOx = 89%
NOx = 80%
NOx = 89%
NOx = 89%
Bottleneck

## Slide 19
19
Lower central air decreases air / fuel ratio in the flame core and leads to less NOx formation
Central air reduction supports lower NOx generation
Source: Unitherm
Primary Air Pressure: 150mbar
Central Air Pressure: 125 mbar
NOx (Kiln Inlet): 2700ppm
Primary Air Pressure: 150mbar
Central Air Pressure: 25 mbar
NOx (Kiln Inlet): 1300ppm

## Slide 20
20
Destroy NOx from main burner and minimize fuel NOx formation by local reducing atmosphere and hot spot in calciner
  Low NOx calciner / MSC
  Fuel mix optimization
    Fuel with high volatile content*
    Lump fuel (small portion at kiln inlet)
    + Low nitrogen fuel
“High” temperature and low oxygen for low NOx in calciner
e.g. petcoke, anthracite
e.g. plastics, lignite
Source: Int. Cement Review, June 1997, p.65ff
*Reactive fuels (e.g. lignite) react so intensely at start of combustion that local reducing conditions occur (+ increased Temp.)

## Slide 21
21
Main reaction: NO reduction with CHx radicals arisen from fuel hydrocarbons during combustion (at high temperatures)
NOx destruction by hydrocarbon radicals in calciner
Reduction of NO by the reaction with NHx radicals (analogous to SNCR mechanism) or other intermediate compounds such as HCN
Additional reduction of NO: heterogeneous at the fuel-coke surface
Minor role: NO reduction by CO or H2 catalyzed by meal (Fe, CaO) NO + CO  N2 + CO2 H2 + NO  N2/NH3 + H2O

## Slide 22
22
Hot spot to be below thermal NOx formation temperature
High temperature (hot spot) for an increased radical pool and higher NO reduction rates …but below (dominant) thermal NOx temperature range > other restrictions regarding hot spot (refractory, build-ups) probably decisive …typical hotspot temperature in ILC ~ 1000-1200°C > flame temperatures in PCC higher (very low l)
Low oxygen zone (local reducing condition) to prevent oxidation of intermediate compounds (the NOx re-formation), the fuel NOx formation and the hydrocarbon combustion … and for NO reduction by CO (catalyzed) > not main mechanism

## Slide 23
23
Mealsplit:
control of hot spot
Air split or main fuel bellow tertiary air connection:
reducing conditions
“MSC”/Staged fuel: Additional “LowNOx burner” or (lumpy) AFR ! Build-ups
Hot spot and Reducing Conditions are the two features to operate a calciner as a “Low NOx Calciner”
 >1
 <1
 >1
1000-
1200°C
Example of a Low-NOx calciner: Prepol MSC




## Slide 24
24
Significant NOx reduction with primary measures in calciner
Experience Ramos Arizpe (Holcim Apasco)
Meal split used to increase calciner hot spot temperature NOx reduction from 1200 to 800 mg NO2 /Nm3 @ 10% (ref. PPE project of Javier Niño)
FLS inline precalciner
Experience St.Geneviève (Holcim US)
e.g. petcoke, anthracite
e.g. plastics, lignite
Source: Int. Cement Review, June 1997, p.65ff
Very good “reburn” in calciner NOx much lower with coal in PC  coke to main burner

## Slide 25
25
Ramos Arizpe increases calciner temperature for low NOx

## Slide 26
26
Revamp of existing installation to a Low-NOx design not possible (e.g. meal split not possible due to height of cyclones etc.)
Hotspot can cause refractory damages if there is no or not an evenly distributed meal curtain, inadequate refractory quality
Reducing conditions influence circulation phenomena and can cause build-ups (increased SO2 release in reducing zone)
Difficult control of meal, fuel, air splits
CO emissions if residence time after reducing zone is too low for burnout
Increase of heat consumption (meal split)
The Low NOx Calciner application is limited

## Slide 27
27
Primary measures to be applied as long as there is no negative process, quality or emission impact
Process optimizations have priority over NOx optimization
Exploit the primary reduction measures potential!
Generally not recommended: Process impacts!
  Low NOx burner with too low primary air
  Water and dust injection (flame cooling) „only“ to prevent NOx emission
  Reducing atmosphere in the kiln
example
Source: VDZ

## Slide 28
28
Potential of NOx reduction measures depends on process conditions – up to ~50% by primary measures
% NOx reduction
Not cumulative

## Slide 29
29
SNCR
  SNCR is the proven secondary abatement technology
SCR
  <10 full scale plants in the cement industry
  Optimization phase ongoing
Secondary NOx reduction measures are the Selective Non-Catalytic Reduction and the Selective Catalytic Reduction
NH2° + NO  N2+ H2O

## Slide 30
30
  SNCR in general enough to comply with current NOx limi
  If low emissions required, risk of NH3 or CO emissions and high cost
  Op. costs: 0.5 - 1.5 USD/tcli
  SCR: Limited experience; several pilots, few full scale plants in industry
  Potential for reduction of other components (e.g. VOC)
  Op. costs: 1 – 2 USD/tcli (?)
Reagent: components containing NH2° (ammonia, urea, …)
NH3
SCR
T° injec.: ~300°C
Red.: up to 95%
Selective Catalytic Reduction
NH3
SNCR
T° injec.: 850-1000°C
Red.: up to 75%
Selective Non Catalytic Reduction
Reduction requires temperature or catalyst

## Slide 31
31
Critical for successful SNCR
  Optimum temperature window: 850-1050oC depending on reagent, gas composition etc. Too low >> NH3 slip Too high >> NOx formation
  Good mixing and sufficient residence time in this window
  Availability of oxygen
Ammonia allows injection at lower temperature
Proper temperature is key for successful SNCR
NO reduction
NH3/NOraw molar ratio = 1
NO reduction in %
NH3 slip in %
Gas temperature in °C
NH3 slip
example
Source curves: ABC&I (generic data)
O2, CO

## Slide 32
32
Improper SNCR performance
  CO or NH3 emissions (ammonia slip)
  High operating costs
  Risk of non-compliances
Improper SNCR performance leads to increased NH3 and/or CO emissions …and to high costs!
Example of SNCR trial
Example of cost consequences SNCR optimization, i.p. change from urea to ammonia: 50% SNCR operation cost saved

## Slide 33
33
The lower the NOx-target at stack, the more important is the efficiency of the SNCR
Chart: NOx-Emission [mg/Nm3]
| 300 | 450 | 600
CHF/t Cli NO 900g/t cli eta 30% | 0.76414 | 0.43914 | 0.11416
CHF/t Cli NO 900 g/t cli eta 45% | 0.50943 | 0.29276 | 0.076109
CHF/t Cli NO 900 g/t cli eta 70% | 0.32749 | 0.18821 | 0.048927
Reagenz Cons t/t Cli | 7.0745 | 5.5117 | 3.949
0.06 CHF/t cli
0.25 CHF/t cli
eta =70%
eta =45%
eta =30%
@ NO 900 g/t cli from the process
Source: Ernst Bucher, Holcim Central Europe

## Slide 34
34
Adequate reagent to minimize consumption and costs
Best injection location for reagent (can change due to stratification)
Adequate reagent distribution
Optimization of reagent control loop
Trials for SNCR optimization and low NOx

## Slide 35
35
Example Ternate: Comparison of different injection levels

## Slide 36
36
Higher efficiencies for Ammonia trials (brownish) compared to Urea (blue) (different plants)
Ammonia is generally the more economic reagent
Guide values Efficiency ~ 55% at Molar Ratio of 1-1,2 (Ammonia)
  ~ 30% at Molar Ratio of 1-1,2 (Urea)
  Molar Ratios < 1.2 : NH3 slip not expected

## Slide 37
37
Urea requires more residence time (water evaporation and urea decomposition)
SNCR - Ammonia vs. Urea
Source: Bernd van der Heide, Minimizing NOx Emissions…, 2001

## Slide 38
38
Material build ups
Urea precipitation
  Inadequate spray pattern
  Efficiency reduction
Potential solutions
  Air Blaster Nozzle
  Flushing (with acidic solution)
Reagent spray pattern disturbances by nozzle clogging to be prevented
Source: Serfain Sanchez

## Slide 39
39
Issues: Measurement delay, CEM vs. injection location, NOx fluctuations
Control loop / PID to be optimized
Trials: Further improvement by including other parameters,
  PH NOx (faster response)
  Kiln inlet NOx (predictive aspect)
  (BZT,…)
Optimization of SNCR control loop to reduce reagent cost
Example PPE project I. Gafner
Process stability reduces reagent consumption!

## Slide 40
40
NOx target 500 mg/Nm3
  Can be achieved in most cases
NOx target 200 mg/Nm3
  Can be achieved in some cases only (optimum conditions)
SCR to be considered in a few cases
  Lower NOx limits
  NH3 limits!
  Increasing reagent cost (consumption, price, availability)
  Odor issues
  …
By exploiting primary measures and applying an optimized high efficient SNCR low NOx emissions can be achieved

## Slide 41
41
41
Where to place the catalyst?
Advantages high dust
  Proper temperature, no re-heating necessary by large heat-exchangers and in most cases (including modern systems) external heat (costs)
  No additional pressure drop of heat exchangers (~10 mbar)
Advantages low dust
  Lower demands for cleaning
  Smaller catalyst-size (smaller pitch-size possible)
  VOC released in raw mill are treated (VOCs from mill not expected in general)
Low dust SCR installation requires reheating

## Slide 42
42
42
High dust SCR plants
  Solnhofen 2001
  Monselice 2006
  Schwenk, Mergelstetten 2010
  Italcementi, Rezzato 2014
Lepol SCR
  Italcementi, Sarche 2007
Low-dust SCR
  Rohrdorf, 2011
  LafargeHolcim, Midlothian 2016
Semi-dust SCR
  LafargeHolcim, Mannersdorf 2012
  LafargeHolci, Joppa 2013
SCR experience in the industry – references (list may not be complete)
SCHEUCH Semi-Dust SCR
RN SCR test plant
Monselice
SCR
Mergelstetten

## Slide 43
43
43
Main challenges for the SCR catalyst is not the NOx reduction, but handling of dust and prevention of poisoning
Vanadium (V2O5) based honeycomb catalyst (standard)
The basic requirements of an SCR catalysts are:
  Suitable to handle gas with dust on the order of 100 g/m3
  Prevention of poisoning, covering (Tl, Ammonia-sulfates…)
  High activity and lifetime
  Selectivity, limitation of unwanted reactions, i.p. oxidation of SO2 to SO3
  Thermal / mechanical stability
  Small pressure loss
Picture: TU Clausthal

## Slide 44
44
44
SNCR optimization by
  Online temperature measurement
  CFD
Flue Gas Circulation
Catalytic bag material
There are new approaches for NOx reduction on the way…
POWITEC heSNCR
Source: Irwin Gafner, PPE EC
FLS CataMax
GORE DeNOx filter

## Slide 45
45
45
Primary measures
  Generally low investment and operating cost for a certain NOx reduction range
  Potential and efficiencies difficult to predict
  Limited by process and quality impact - process optimizations have priority over NOx optimization
Secondary measures
  Run SNCR if necessary (after exploiting primary measures to reduce reagent costs)
  SNCR to be optimized to lower operation costs, to prevent negative consequences (CO, NH3) and to increase the deNOx potential (ammonia in general more economic than urea)
  Catalytic reduction in future as a multi-pollutant reduction technology
NOx Summary – Exploit primary and optimize secondary measures for a successful and economic NOx reduction

## Slide 47
47
47
SCR costs around 10 Mio. CHF
CapEx
  Engineering, Material, Erection, Commissioning and Training ~5.0 Mio. CHF
  Ventilator, dust transport, injection system, gas analyzer ~1.5 Mio. CHF
  Civil work, steel construction ~2.5 Mio. CHF
  Electronics/Cabling ~1.0 Mio. CHF
  Fees and permits ~0.3 Mio. CHF
  Total ~10 Mio. CHF
Operation costs
  Depending on conditions ~1 CHF/tcli assuming no exhaust re-heating and 4 years catalyst lifetime