## Slide 1: Combustion Engineering
Technical Development Program for Process Performance Engineers – SPREAD 2016
Mirko Weber

## Slide 2
2
Know how to calculate the gas flows in a kiln system
Know what is contributing to the gas flows in a kiln system
Know how to check the amount of false air in a kiln system
Learning Objectives

## Slide 3
3
Basic Definitions
Gasflow Calculations
False Air Investigation
Content

## Slide 4
4
Actual conditions (of gas flow)
  actual absolute pressure (ambient + Δp: ~ 750-1030 mbar)
  actual temperature (~ -20°C to 1500°C)
Normal conditions → Nm3
  1013 mbar (ambient pressure at sea level)
  273.15 K (water freezing temperature = 0°C)
Standard conditions (US) → scf (standard cubic foot)
  30 inch Hg (1016 mbar)
  60°F (15.6°C = 288.7 K)
Basic Definitions
Gas flow is calculated in Nm3

## Slide 5
5
Basic Definitions
Gasflow Calculations
False Air Investigation
Content

## Slide 6
6
Mass flows in & out of the kiln system
Gasflow Calculations
Raw meal
Clinker
False air
False air
False air
False air
False air
False air
False air
False air
Fuel
Air
Exhaust gas
Air

## Slide 7
7
C
H
O
N
S
Ash
H2O
C + O2→ CO2
S + O2 → SO2
H + O2→ H2O
N → N2
Ash
Air
(N2, O2) + H2O
Fuel
Heat
Gasflow Calculations
What are the combustion reactions and products?

## Slide 8
8
Required air for complete combustion without any excess of oxygen (stoichiometric combustion)
Sum of all combustion gases from a stoichiometric combustion (CO2, SO2, N2, H2O), including the humidity of the fuel and the inert parts of the combustion air (N2, H2O)
Minimum combustion air → Amin
Minimum exhaust gas → Vmin
Gasflow Calculations
Amin and Vmin

## Slide 9
9
Comp.
Calculation
Nm3/kgcoal
C
8.89 x 71%
6.312
H
26.6 x 4%
1.064
S
3.3 x 1%
0.033
O
-3.3 x 6%
- 0.198
Total
7.211
Amin = 7.21 Nm3/kgcoal = 0.26 Nm3 /MJ
Example (bituminous coal):
  CVnet = 28 MJ/kg
  C = 71%
  H = 4 %
  O = 6%
  N = 1.5%
  S = 1%
  H2O = 0.5%
  Ash = 16%
Amin = 8.89 x C + 26.6 x H + 3.3 x S - 3.3 x O [Nm3/kgfuel]
C, H, S, O must be weight fractions !
Gasflow Calculations
What is Amin for the combustion of 1kg fuel?

## Slide 10
10
Vmin = 1.87 x C + 0.8 x N + 0.79 x Amin + 0.7 x S + 11.2 x H + 1.24 x H2Ofuel+ H2Oair x Amin [Nm3/kgfuel]
C, N, H, S, H2O must be weight fractions !
Comp. | Calculation | Nm3/kgcoal | %Vmin
CO2 | 1.87 x 71% | 1.328 | 17.2
N2 | 0.8 x 1.5% + 0.79 x 7.21 | 5.709 | 74.0
SO2 | 0.7 x 1% | 0.007 | 0.1
H2O | 11.2 x 4% + 1.24 x 0.5% + 3% x 7.21 | 0.671 | 8.7
Total |  | 7.72 | 100
Example (bituminous coal):
Vmin,wet = 7.72 Nm3/kgcoal = 0.28 Nm3 /MJ
Vmin,dry
Gasflow Calculations
What is Vmin for the combustion of 1kg fuel?

## Slide 11
11
Minimum combustion air Amin
Amin ≈ 0.26 Nm3/MJ
Minimum exhaust gas Vmin
Vmin,wet ≈ 0.28 Nm3/MJ (wet)
Vmin,dry ≈ 0.25 Nm3/MJ (dry)
Gasflow Calculations
Approximate values for Amin and Vmin can be used for gas flow calculations

## Slide 12
12
Fuel
Anthracite, Petcoke at 1% humidity
Bituminous coal at 1...2% humidity
Lignite (high humidity) at 10% humidity
Wood / Peat at 10...15% humidity
Light oil
Heavy oil (bunker C)
Tar
Waste tires (rubber)
Natural gas (high CH4 content)
Natural gas (approx. 24% C2H6)
Amin-Factor
Vmin-Factor
(Nm3/MJ)
(Nm3/MJ)
0.26 0.27
0.26 0.28
0.26 0.29
0.26 0.30
0.26 0.29
0.26 0.28
0.26 0.28
0.26 0.27
0.27 0.30
0.26 0.30
Gasflow Calculations
Approximate values (for Amin & Vmin) fit well for most type of fuels

## Slide 13
13
CO2
H2O
These factors apply for a dry kiln!
H2Ovapor ≈ 0.01 Nm3/kgcli
CO2,raw meal ≈ 0.27 Nm3/kgcli
→ from raw meal decarbonization
→ from hydrated water in raw meal
Approximate factors for exhaust gas contribution from raw meal
Gasflow Calculations
Raw meal contributes CO2 and (some) H2O to exhaust gas flow

## Slide 14
14
Kiln exhaust gas
air
False
Excess air O2, N2
Vmin,dry
CO2, SO2, N2
H2O
Vmin,wet
Air
Amin
Raw meal
H2O
Fuel
CO2
Gasflow Calculations
Fuel, raw meal and air contribute to total kiln exhaust gas

## Slide 15
15
H2Ovapor
Excess Air
Vmin,dry
&
CO2,raw meal
Kiln exhaust gas
air
False
Excess air O2,N2
Vmin,dry
CO2,SO2,N2
H2Ovapor
Vmin,wet
Air
Amin
H2O
Fuel
CO2
Mcli = clinker production rate [kgcli/h] q = spec. heat consumption [MJ/kgcli]
CO2,raw meal
Vmin,dry
Gasflow Calculations
Dry exhaust gas from combustion and raw meal

## Slide 16
16
O2,dry % = measured (dry) O2 concentration
Vmin,dry
&
CO2,raw meal
H2Ovapor
Excess Air
air
False
Excess air O2,N2
Vmin,dry
CO2,SO2,N2
H2Ovapor
Vmin,wet
Air
Amin
H2O
CO2
Fuel
Kiln exhaust gas
Excess air (including False air)
Gasflow Calculations

## Slide 17
17
Vmin,dry
&
CO2,raw meal
H2Ovapor
Excess Air
Kiln exhaust gas
air
False
Excess air O2,N2
Vmin,dry
CO2,SO2,N2
H2Ovapor
Vmin,wet
Air
Amin
H2O
CO2
H2Oraw meal
(Vmin,wet - Vmin,dry)
Fuel
Mcli = clinker production rate [kgcli/h]
q = spec. heat consumption [MJ/kgcli]
Moisture
Gasflow Calculations

## Slide 18
18
Gasflow Calculations
Total kiln exhaust gas
Vmin,dry
&
CO2,raw meal
H2Ovapor
Excess Air
from raw meal
from combustion
excess air (based on dry O2 measurement)
Kiln exhaust gas

## Slide 19
19
at kiln system outlet
Gasflow Calculations
Typical exhaust gas quantities & compositions for different kiln systems

## Slide 20
20
Precalciner Fuel Dosing
Kiln Fuel Dosing
Clinker
Suspension Preheater
Kiln ID Fan
Meal Dosing
Precalciner
Burner
Tertiary Air
Kiln inlet
%decarb decarbonization degree of hot meal at kiln inlet
→ at kiln inlet, part of CO2 of raw meal already gone
%PC thermal energy input at pre-calciner
→ at kiln inlet, only fuel in main firing contributes to Vmin
Mcli clinker production rate
q kiln heat consumption (total)
O2,dry% O2 at kiln inlet
Gasflow Calculations
Gas flow at kiln inlet for a kiln with pre-calciner

## Slide 21
21
Basic Definitions
Gasflow Calculations
False Air Investigation
Content

## Slide 22
22
How much false air is entering into the kiln system between preheater exit and ID-Fan?
What is the total exhaust gas flow at the ID-Fan
False air investigation
False Air Investigation

## Slide 23
23
Vmin,dry
&
CO2,raw meal
Excess air
EPHexit
H2Ovapor
Vmin,dry
&
CO2,raw meal
Excess air EID-Fan
H2Ovapor
air
False
1
CT
Water
Preheater Exit
ID-Fan
False Air Investigation
2
False Air = EID-Fan – EPHexit
Exhaust gas composition at PH exit and ID-fan
Kiln exhaust gas

## Slide 24
24
Dry exhaust gas flow at preheater exit
Excess air at ID-Fan
Excess air at preheater exit
False air intake between PH exit and ID fan
False Air Investigation
1) False air intake between PH exit and ID-fan

## Slide 25
25
False Air Investigation
2) Total exhaust gas flow at ID-Fan

## Slide 26
26
Fuel, raw meal & air contribute to total exhaust gas flow → additional inputs, e.g. water injection (cooling tower)
Total exhaust gas flow is calculated with
  clinker production rate
  specific heat consumption
  O2 concentration
False air intake is determined by O2 measurement at the different locations in the kiln system
Summary

## Slide 27
PPE/Combustion Engineering, 2013-11-072015-08-04
27
27
Any false air intake increases heat consumption, increases power consumption or reduces production capacity (if ID-fan limited)
Determine and reduce the amount of false air in your kiln system frequently
Key messages

## Slide 29
PPE/Combustion Engineering, 2013-11-072015-08-04
29
29
Additional Information

## Slide 30
PPE/Combustion Engineering, 2013-11-072015-08-04
30
30
atoms & molecules
1 kmol are 6.02 · 1026 molecules
Molecules → mol → Nm3
Basic Definitions
=
Ideal gas law:
R: universal gas constant
R = 8.314 kJ/kmol/K
n: mole number [kmol]
atom: e.g. C, H, O, N, S
=
=
=
molecule: group of atoms, → e.g. CO2, N2, O2, H2O, CH4
Avogadro constant
At normal conditions 1 kmol of gas occupies 22.4 m3 of volume
1 kmol = 22.4 Nm3

## Slide 31
PPE/Combustion Engineering, 2013-11-072015-08-04
31
31
The formula below is used to convert gas flows of ideal gases from normal conditions (0°C, 1’013 mbar) to actual conditions (T, p) in the process.
Vact gas flow at actual conditions in m3/s
Vnorm gas flow at normal conditions in Nm3/s
Tact actual gas flow temperature in °C
pact = pambient + pmeasured,relative actual absolute pressure in mbar
Gas flow conversion from Nm3 to actual conditions
ambient pressure
measured pressure difference
Basic Definitions
Ideal gas law:
R: universal gas constant
R = 8.314 kJ/kmol/K
n: mole number [kmol]

## Slide 32
PPE/Combustion Engineering, 2013-11-072015-08-04
32
32
Mcli clinker production rate (kgcli/h)
R kiln feed to clinker ratio = 1/[(1-LOIKF)·(1-dustloss)] (kgKF/kgcli)
H2Ocryst % crystal water (chemically bonded water) (kgH2O/kgKF)
w % moisture content of raw meal (kgH2O/kgRM)
LOIKF loss on ignition of kiln feed (kgLOI/kgKF)
LOIFD loss on ignition of filter dust (extracted kiln dust) (kgLOI/kgFD)
dustloss % dust leaving kiln system (wet: smoke chamber, dry: PH exit) (kgFD/kgKF)
H2O from raw meal/slurry moisture
CO2 from raw meal
Gasflow Calculations
For wet kilns and/or if kiln dust is extracted and discarded
Gases from kiln feed/raw meal (detailed calculation)

## Slide 33
PPE/Combustion Engineering, 2013-11-072015-08-04
33
33
Gasflow Calculations
Excess air (including False air)
O2,dry % = measured O2 concentration
Vmin,dry
&
CO2,raw meal
H2Ovapor
Excess Air
G
X
21% O2
79% N2
O2,dry %
condensed before measurement
Kiln exhaust gas

## Slide 34
PPE/Combustion Engineering, 2013-11-072015-08-04
34
34
Gasflow Calculations
False air intake
FA [%] = additional false air as fraction of flow before false air intake
VFA intake [Nm3/h] = false air intake
VGas,in,dry [Nm3/h] = gas flow (dry) before false air intake
%O2,in [%] = measured O2 concentration (dry) before intake
%O2,out [%] = measured O2 concentration (dry) after intake
Important! If it is not possible to measure the O2 before and after the intake simultaneously, the two measurements have to be corrected for the O2 variation in the gas flow, e.g. by comparison to the O2 signal at PH exit.

## Slide 35
PPE/Combustion Engineering, 2013-11-072015-08-04
35
35
Heat of Combustion referred to 25°C
→ including condensation of H2O
→ measured in bomb calorimeter
CVgross - H2Ocombustion ∙ 2450 kJ/kgH2O
CVgross =
CVnet =
Gross Calorific Value
Net Calorific Value
CVgross - (H2Ofuel+ 9 H) ∙ 2450 kJ/kgH2O
Basic Definitions
Bomb calorimeter
→ measurement of CVgross
→ CVnet calculated with formula below
Gross & Net Calorific Values