## Slide 1: Introduction Dedusting
Technical Development Program for Process Performance Engineers – SPREAD 2016
Mirko Weber

## Slide 2
2
Why Dust Control ?

## Slide 3
3
Why Dust Control ?
Reducing health hazard possibilities
Assuring compliance with existing regulations
Reducing cleanup and maintenance cost
Reducing equipment wear and downtime
Increasing visibility and reducing probability of accidents
Reducing troubles in community relation
More pleasant working condition thus improving employee morale and productivity
Possible product savings

## Slide 4
4
Legacy Holcim 2012: Around 35% EP‘s
Kiln/Raw Mill Filters - EP’s get less, however there is still a significant amount in LafargeHolcim
Total 185
Total 217
Legacy Holcim 2009: Around 50% EP‘s

## Slide 5
5
Around 20% above 50 mg/Nm3
Around 55% below 20 mg/Nm3
EP performance lower compared to BF
Almost all Bag Filters run below 20 mg/Nm3
Almost half of the EP’s run above 50 mg/Nm3
Total 144 reported
Source: PEP 2009

## Slide 6
6
Available collecting area
Moisture content in raw gas
Gas temperature
Gas velocity (False air!)
Dust content in raw gas
Dust properties (resistivity, particle size distribution)
Power input
Availability (CO peaks!)
Cleaning efficiency of Electrostatic Precipitator depends on various parameters

## Slide 7
7
Change of fuel mix (more “difficult” fuel):
  More CO peaks due to instable combustion (fuel feed, net calorific value – e.g.)
  Higher gas flow rate (due to higher heat consumption or false air)
  More Cl, SO3, NH3, organics can lower the EP performance
Transition phase during mill start with higher dust emission
  higher temperature at EP inlet (gasflow/dew point)
Changed conditions can have an impact on EP performance
95°C
EP inlet temperature
time
Mill ON
Dust Emission

## Slide 8
8
Process dependence of EP while BF unaffected by process conditions within a wide range
Optimization potential EP: precipitation, gasflow, power  references show 50 mg/Nm3 or 20 mg/Nm3 possible with EP upgrade!  lower CAPEX compared to conversion
Disadvantage BF: delta P, waste (bags), temperature limited, potential selective dust collection only in EP
Convert the EP to a Bagfilte?

## Slide 9
9
General Description of a “Pulse Jet” Bag Filter
Raw gas chambers with bags
Raw gas duct inlet to dedusting chambers
Clean gas and “Pulse Jet” cleaning injectors
Hopper and conveyor for dust collection
Clean gas plenum
Penthouse for regular maintenance
Scheuch
Collecting duct and filter outlet

## Slide 10
10
Pulse Jet Bag Filter Main Figures
Dust emission
  <10-20 mg/Nm3 independent from process
  No transient operation influence
  No CO issue (no ignition source)
Bags
  Length: 3.5 to 10 m
  Air-to-Cloth: 1.0 m3/(min*m2)
Operating temperature
  120°- 230°C max.
Pressure drop flange to flange
  10 - 15 mbar
Compressed air for bags-cleaning
  0.5 – 4 bar
Bag life time
  4 years and more

## Slide 11
Case Study Typical Problems in a Bagfilter
Short bag life time
Dust emission
Corrosion
High pressure drop