## Slide 1: Tools day - Standard Tools from TT
Technical Development Program SPREAD 2016

## Slide 2: Objectives/Coaches of the day
Get to know the Thermal Technology Standard tools
Be able to use the tools in order to detect areas for optimization and define related actions
Learn how to interpret measurement results
Know common guide values
Be able to benchmark your kiln system

## Slide 3: Time planning/Tools Required
  Required tools
Paper and Pen
Pocket calculator
Laptop
PPE Reference guide
Handouts and files will be distributed by coaches
Program
Introduction to tools, preparation and measurements by tool responsible in plenum
Detailed discussion and hands-on application of tools in groups
Wrap-up and summary in groups
Do calculations individually
Notes: Time plan is fake not real one!!!

## Slide 4: Group Formation

## Slide 5: Practical Afternoon Posts
 | Group A | Group B | Group C | Group D
10:30 12:05 | Burner Check | Heat Balance | PH Profile | Cooler Air
12:10 14:45 | Cooler Air | Burner Check | Heat Balance | PH Profile
14:50 16:35 | PH Profile | Cooler Air | Burner Check | Heat Balance
16:40 18:10 | Heat Balance | PH Profile | Cooler Air | Burner Check

## Slide 6: Updated Timing Guideline
Time | Standard Tools & Measurements | Responsible
08:30 - 09:00 | Introduction | Stefan Gross
09:00 - 09:45 | A/S tool | Stefan Gross
09:50 - 10:05 | 1st tool | Coaches
 | Coffee Break | 
10:30 - 11:30 | 1st tool (cont’d) | Coaches
11:35 - 12:50 | 2nd tool | Coaches
 | LUNCH | 
14:00 - 15:15 | 3rd tool | Coaches
15:20 - 15:35 | 4th tool | Coaches
 | Coffee Break | 
15:40 – 16:40 | 4th tool (cont’d) | Coaches
16:45 - 17:30 | Summary of the process problems and of the findings | Groups

## Slide 7: Introduction
=
Standard Measurements = Check Routines

## Slide 8: Introduction
one year
 Required before and after major modifications or process changes of the kiln system
Burner - Check
Combustion - Check
Heat- & Mass - Balance
every two years

False Air Investigation

Alk-Sulphur-Cl Balance

Instrumentation Check

Calibration of Feeders

Cooler Air Distribution

T & p profile in PH
yearly kiln stop
Frequency of Standard Measurements for Kilns

## Slide 9: Introduction
Preconditions for standard measurements
  Stable and representative kiln operation
  Kiln close to nominal production rate
  Stable and normal coating situation
  No major process adjustments in the last 24 h

## Slide 10: Situation
Dear Plant Manager
Notes: Not shown, Plant manager will show the letter with the presenter..

## Slide 11: Kiln System Design
5 stage precalciner kiln
Inline calciner (5s residence time)
High momentum burner
Grate cooler with fixed inlet
Ter. Air
Ter. Air
Fuel
Fuel
Meal

## Slide 12: Kiln System Operation
Fuels:
  Coal / Petcoke mix (80/20)
  Fluff (2.03 t/h at main burner)
  Plastics (4.26 t/h at precalciner)
Availability: 87%, Production rate index: 92%
  Several stops for riser duct and cyclone cleaning
Clinker temperature causes problems with belt to cement mill
Tertiary air damper removed due to abrasion
ID fan close to maximum speed

## Slide 13: Downtime Pareto

## Slide 14: Kiln Stop Pareto

## Slide 15: Main Tasks
Analysis of kiln operation : paretos, operation and quality trends long/ short term (TIS, LIMS,…)
Assessment of kiln line
  heat balance
  burner check
  cooler air distribution
  alkali-sulfur-chlorine balance
  preheater assessment
Evaluation of measurements and conclusions
Define required steps to overcome current issues and to achieve defined targets